## Slide 1: Logan Xcoder Library API

## Slide 2: Overview
Define External User Interface for the Logan Xcoder Library
Xcoder Codec User API
Define Internal FW Interface for the Logan Xcoder Library
Xcoder NVMe FW API

## Slide 3: [External API] Xcoder Codec User API

## Slide 4: Xcoder Codec User Interface
Command | Parameters | Description
xcoder_dec_open | XCoderContext XCoderConfig | User opens a decoder instance
xcoder_dec_close | XCoderContext | User closes a decoder instance
xcoder_dec_send | XCoderContext XCoderPacket | User sends compressed video packets to the decoder instance. Null data to flush decoder
xcoder_dec_receive | XCoderContext XCoderFrame | User gets a decoded YUV frame from the decoder instance

## Slide 5: Xcoder Codec User Interface (Cont’)
Command | Parameters | Description
xcoder_enc_open | XCoderContext XCoderConfig | User opens a encoder instance
xcoder_enc_close | XCoderContext | User closes a encoder instance
xcoder_enc_send | XCoderContext XCoderFrame | User sends a YUV frame to the encoder instance. Null data to flush encoder
xcoder_enc_receive | XCoderContext XCoderPacket | User gets a encoded video packet from the encoder instance
Xcoder_codec_connect | XCoderContext XCoderContext | User connects a decoder to an encoder on same device space.

## Slide 6: Xcoder Codec User Interface (Cont’)
Command | Parameters | Description
init_pts_table |  | Initialize a table for each packet’s PTS/FrameOffset entry
register_pts_timestamp | Timestamp Frame Offset | Registers packet PTS timestamp and video stream frame offset in the PTS vs FrameOffset table.
retrieve_pts_timestamp | Timestamp Frame Offset | Retrieves packet PTS timestamp and video stream frame offset in the PTS vs FrameOffset table.

## Slide 7: XCoderContext
typedef struct _XCoderContext {
/* Device Card ID */
int card_id;
/* Codec ID */
unsigned int xcoder_hw_id;
unsigned int xcoder_inst_id;
unsigned int xcoder_type;
void* pts_table;
} XCoderContext;

## Slide 8: XCoderConfig
typedef struct _ XCoderConfig {
/* Device Card ID */
int card_id;
/* Codec ID */
unsigned int xcoder_hw_id;
unsigned int xcoder_inst_id;
/* Custom Configuration Data */
unsigned int template_config_id;
void* config_data;
} XCoderConfig;

## Slide 9: XCoderPacket
typedef struct _ XCoderPacket {
long long pts;
long long dts;
unsigned int end_of_stream;
unsigned int start_of_stream;
unsigned int video_width;
unsigned int video_height;
unsigned int data_len;
void* data;
} XCoderPacket;

## Slide 10: XCoderFrame
typedef struct _ XCoderFrame {
long long pts;
long long dts;
unsigned int end_of_stream;
unsigned int start_of_stream;
unsigned int video_width;
unsigned int video_height;
unsigned int data_len[3];
void* data[3];
} XCoderFrame;

## Slide 11: Sample Usage: Open Decoder
XCoderContext dec_ctx;
XCoderConfig dec_conf;
dec_conf.card_id = dev_fd;
dec_conf.xcoder_hw_id = 0;
dec_conf.xcoder_inst_id = 0;
err = xcoder_dec_open(&dec_ctx, &dec_conf);

## Slide 12: Sample Usage: Open Encoder
XCoderContext enc_ctx;
XCoderConfig enc_conf;
enc_conf.card_id = dev_fd;
enc_conf.xcoder_hw_id = 0;
enc_conf.xcoder_inst_id = 0;
enc_conf.template_config_id = 0xFF;
enc_conf.config_data = custom_data;
err = xcoder_dec_open(&enc_ctx, &enc_conf);

## Slide 13: Sample Usage: Send Data to Decoder
XCoderPacket packet;
packet.video_width = 1920;
packet.video_height = 1080;
packet.start_of_stream = start_flag;
packet.end_of_stream = end_flag;
packet.data = video_data;
packet.data_len = video_data_size;
err = xcoder_dec_send(&dec_ctx, &packet);

## Slide 14: Sample Usage: Send Data to Encoder
XCoderFrame frame;
frame.video_width = 1920;
frame.video_height = 1080;
frame.start_of_stream = start_flag;
frame.end_of_stream = end_flag;
frame.data[0] = video_data;
frame.data_len[0] = video_data_size;
xcoder_enc_send(&enc_ctx, &frame);

## Slide 15: Sample Usage: Receive Data from Decoder
XCoderFrame frame;
frame.data[0] = data_buffer;
err = xcoder_dec_receive(&dec_ctx, &frame);
//frame.data[0] contains Y frame data
//frame.data[1] contains Cb frame data
//frame.data[2] contains Cr frame data
Y_frame_size = frame.data_len[0];
Cb_frame_size = frame.data_len[1];
Cr_frame_size = frame.data_len[2];
end_flag = frame.end_of_stream;
data_size = frame.data_len;
video_width = frame.video_width;
video_height = frame.video_height;

## Slide 16: Sample Usage: Receive Data from Encoder
XCoderPacket packet;
packet.data = data_buffer;
err = xcoder_enc_receive(&enc_ctx, &packet);
//packet.data contains video data
end_flag = packet.end_of_stream;
data_size = packet.data_len;
video_width = packet.video_width;
video_height = packet.video_height;

## Slide 17: [Internal API] Xcoder NVMe Commands

## Slide 18: Xcoder NVMe Commands
Command | Description
nvme_admin_xcoder_open | Initialize and configure a decoder/encoder instance
nvme_admin_xcoder_close | Destroy a decoder/encoder instance
nvme_admin_xcoder_connect | Connect a decoder instance with an encoder instance
nvme_cmd_xcode_write | Send a compressed video packet or a YUV frame to a decoder/encoder instance
nvme_cmd_xcode_read | Get a compressed video packet or YUV frame from a decoder/encoder instance

## Slide 19: nvme_admin_xcoder_open (opcode: 0xC0)
CDW10 bits | Description
31:30 | Xcoder HW Id: 0-XCODER_ID_DECODER0 1-XCODER_ID_DECODER1 2-XCODER_ID_ENCODER
29:24 | Xcoder Instance Id: 0 to 63
23:16 | Template Configuration ID: 0xFF is Custom Configuration Data
15:0 | Length of Custom Configuration Data
prp1/prp2 | Description
Data Length / Data Location | Length of Custom Configuration Data in bytes / Location of Custom Configuration Data

## Slide 20: NVMe Admin Xcoder Open Completion
If status code is == Invalid Field in Command, the command specific field will identify the reason.
If completion is success Host can start issue write command to the decoder or encoder
Value DW0 | description
0xC0 | Invalid xcoder ID
0xC1 | Unsupported template configuration Id

## Slide 21: nvme_admin_xcoder_close (opcode: 0xC1)
CDW10 bits | Description
31:30 | Xcoder HW Id: 0-XCODER_ID_DECODER0 1-XCODER_ID_DECODER1 2-XCODER_ID_ENCODER
29:24 | Xcoder Instance Id: 0 to 63
23:0 | Reserved

## Slide 22: NVMe Admin Xcoder Close Completion
Value DW0 | description
0xC0 | Invalid xcoder ID
0xC1 | Codec Already Closed / Not Opened

## Slide 23: nvme_admin_xcoder_connect (opcode: 0xC2)
CDW10 bits | Description
31:30 | SRC Xcoder HW Id: 0-XCODER_ID_DECODER0 1-XCODER_ID_DECODER1 2-XCODER_ID_ENCODER
29:24 | SRC Xcoder Instance Id: 0 to 63
23:22 | DST Xcoder HW Id: 0-XCODER_ID_DECODER0 1-XCODER_ID_DECODER1 2-XCODER_ID_ENCODER
21:16 | DST Xcoder Instance Id: 0 to 63
15:0 | Reserved

## Slide 24: NVMe Admin Xcoder Connect Completion
Value DW0 | description
0xC0 | Invalid src xcoder ID
0xC1 | Invalid dst xcoder ID

## Slide 25: nvme_cmd_xcoder_write (opcode: 0x80)
CDW10 bits | Description
31:30 | Xcoder HW Id: 0-XCODER_ID_DECODER0 1-XCODER_ID_DECODER1 2-XCODER_ID_ENCODER
29:24 | Xcoder Instance Id: 0 to 63
23:16 | Data Format: 0-XCODER_DATA_FORMAT_VIDEO_PACKET 1-XCODER_DATA_FORMAT_YUV_FRAME
*Assuming 128KB limit lifted for Xcoder
prp1/prp2 | Description
Data Length / Data Location | Length of Data in bytes / Location of Data to Write

## Slide 26: nvme_cmd_xcoder_write (Cont’)
CDW10 bits | Description
15 | End Of Stream Flag 0-FALSE 1-TRUE
14 | Start Of Stream Flag 0-FALSE 1-TRUE
13 | Reserved
12:0 | Metadata Size (in bytes, default: 0) 0 -No Metadata in stream >0-Size of Metadata appended before stream data
*Meta data is embedded inband, appended before the stream data. Size of meta data sent with stream is indicated in the write command. Zero means no meta data embedded.
CDW11 bits | Description
31:0 | Size of data in bytes

## Slide 27: nvme_cmd_xcoder_write (Cont’)
CDW12 bits | Description
31:16 | Video Frame Width
15:0 | Video Frame Height

## Slide 28: NVMe Xcoder Write Completion
DW0 will always carry the available length after write command success or current available space if it not success.
Status code could be success 0x00h, or Invalid Field in Command 0x02h with status code type Generic Command Status.
When no enough space, status code “WAIT” 0xC2 and status code type is Vendor Specific 7h.
DW0 bits | description
31:24 | Reserved
23:0 | Length of available space to write in bytes

## Slide 29: nvme_cmd_xcoder_read (opcode: 0x81)
CDW10 bits | Description
31:30 | Xcoder HW Id: 0-XCODER_ID_DECODER0 1-XCODER_ID_DECODER1 2-XCODER_ID_ENCODER
29:24 | Xcoder Instance Id: 0 to 63
23:16 | Data Format: 0-XCODER_DATA_FORMAT_VIDEO_PACKET 1-XCODER_DATA_FORMAT_YUV_FRAME
15:0 | Reserved
*Assuming 128KB limit lifted for Xcoder
prp1/prp2 | Description
Data Length / Data Location | Length of Data in bytes / Location of Data to Read
CDW11 bits | Description
31:0 | Max size of data to be returned in bytes

## Slide 30: NVMe Xcoder Read Completion
Xcoder will check how many bytes is available and transfer them to host, and send completion with success
If xcoder has not H265 output yet it will completion with zero bytes, the host required to wait for time and re-issue the read command again.
Meta data is embedded in-stream, appended before stream. Size of meta data returned with stream is indicated in the read completion command. Zero means no meta data embedded.
DW0 bits | description
31 | If it 1 indicate this is the end of entire video image
30:25 | Embedded Meta Data Size in bytes
24:12 | Video Frame Width
11:0 | Video Frame Height
DW1 bits | description
31:0 | Total size of returned data in bytes

## Slide 31: NVMe Xcoder Read Completion (Cont’)
Embedded Meta Data Format:
Meta data | Description
Byte 0 | Signature – Fixed pattern to identify start of metadata
Byte 1 | Video Frame Length – Size of video data excluding meta data
Byte 2 | Input Frame Offset – Info obtained for each decoder’s output frame to associate the input video data that it decodes from. It is relayed to the encoder and/or the host for timing synchronization.
Byte 3 | Reserved